## Slide 1: A fair comparison technique for fluid-structure interaction coupling algorithms
Jason P. Sheldon
Scott T. Miller
Jonathan S. Pitt
Distribution Statement A
Approved for public release
Distribution unlimited
deal.II workshop: August 20th, 2013

## Slide 2: Presentation outline
Background
  Motivation
  General FSI concepts
  Governing theory
FSI Testing
  Turek and Hron FSI benchmark
deal.II implementation
  Overview
  Challenge areas
  Future work

## Slide 3: Motivation
Fluid-Structure Interaction (FSI)
  The interaction of a deformable or elastic structure with the surrounding fluid
Motivating Goal
  Analyze the effects of transient wake-induced loads on structures and the resultant flow

## Slide 4: Motivation
Application areas of practical importance
  Wake-structure interaction

## Slide 5: Motivation
Application areas of practical importance
  Wake-structure interaction
  Flexible composite propulsion systems
Notes: Airborne International Composites’

## Slide 6: Motivation
Application areas of practical importance
  Wake-structure interaction
  Flexible composite propulsion systems
  Biomedical applications
  etc.
Notes: Airborne International Composites’

## Slide 7: Motivation
Discovery
  Multiple coupling types, some easier than others
Question
  Which is best?
Literature review
  Michler says that partitioned is better
  Heil says that monolithic is better
  Degroote says that it depends
Common point
  Lack of strict convergence tolerances

## Slide 8: Goal: Impartial comparison
Same governing equations
Same discretization strategies
Same coupling strength
  Same convergence criterion
Same finite element implementation
  deal.II
Same test case
  Turek and Hron FSI Benchmark
  Same mesh
Different coupling algorithms

## Slide 9: Solid/Mesh governing equations
Elasticity
  Lagrangian frame
    St. Venant Kirchhoff model (solid)
    Hookean model (mesh)

## Slide 10: Fluid governing equations
Incompressible Navier-Stokes
  Arbitrary Lagrangian-Eulerian (ALE) frame

## Slide 11: Discretization
Standard numerical discretizations
Spatial
  Bubnov-Galerkin finite element method
    Taylor Hood elements for fluid
Temporal
  Crank-Nicolson method

## Slide 12: General FSI problem
Fluid Domain
Solid Domain
Fluid Boundary
Solid Boundary
Fluid-Solid Interface
ΓFS

## Slide 13: Partitioned FSI coupling
Segregated solves
Iterative interface conditions
  Traction continuity
  Velocity continuity
  Admissible mesh displacements
(Dirichlet-Neumann)
Solve
fluid system
of equations
tn
Convergence check
Solve
solid system
of equations
Solve
mesh system
of equations
tn+1
Solid relaxation
No
Yes

## Slide 14: Quasi-Direct FSI coupling
Combination of simultaneous and segregated solves
  Solid and fluid
    Single algebraic system
  Iterative mesh displacement
    Same as partitioned
One conforming velocity field
  Implicit traction continuity
Solve coupled
fluid and solid system
of equations
Convergence check
Solve
mesh system
of equations
No
tn
tn+1
Yes

## Slide 15: Monolithic FSI coupling
Solve coupled
fluid, solid, and mesh system
of equations
tn
tn+1
Simultaneous solves
  Single algebraic system for everything
One conforming velocity field
  Implicit traction continuity
One-way strong mesh displacement
  Care must be taken to avoid having the mesh affect the solid displacement

## Slide 16: Convergence Criterion
We use the same criterion for the partitioned and quasi-direct fixed-point iterations as for the monolithic Newton-Raphson iterations
This is satisfied when the fluid-solid interface does NOT move between iterations

## Slide 17: The Turek-Hron FSI benchmark

## Slide 18: Benchmark visualization

## Slide 19: Benchmark results
Displacement
Drag and Lift
FSI2 fluid-structure interface lift vs. time:
monolithic and quasi-direct closer match than partitioned
FSI2 fluid-structure interface drag vs. time:
monolithic and quasi-direct closer match than partitioned
FSI2 flag tip x-displacement vs. time:
monolithic and quasi-direct closer match than partitioned
FSI2 flag tip y-displacement vs. time:
excellent agreement for all coupling methods

## Slide 20: Benchmark results: Extrema
Quasi-Direct

## Slide 21: Monolithic wins… this time
Quasi-Direct
Caveat: 2D, Laminar, Low Re, Serial

## Slide 22: Research summary
Developed a computational FSI model
  Three coupling types
  Identical framework and convergence criteria
Turek-Hron benchmark case
  All coupling types equally tightly coupled
  Good agreement for all data
Monolithic coupling (Also quasi-direct)
  Slightly more accurate than partitioned
  Significantly faster than partitioned

## Slide 23: deal.II implementation: Overview
Parameters
Triangulation
FE spaces
Etc.
fsi_handler
3 x 3 BlockSparseMatrix
3 x 1 BlockVector (s)
Monolithic
Quasi-Direct
Partitioned

## Slide 24: deal.II implementation: Overview
Parameters
Triangulation
FE spaces
Etc.
fsi_handler
3 x 3 BlockSparseMatrix
3 x 1 BlockVector (s)
Monolithic
Quasi-Direct
Partitioned
Fluid system assembly
Solid system assembly
Mesh system assembly
Solve and post process
“Couple”

## Slide 25: FEsystem
Input
  Solid FE space = FESystem[FE_Q(p)^d-FE_Q(p)^d]
  Fluid FE space = FESystem[FE_Q(p)^d-FE_Q(p-1)]
  Mesh FE space = FESystem[FE_Q(p)^d]
FETools::get_fe_from_name
hp::FECollection
Output
  Solid FE Space: FESystem<d>[FE_Q<d>(p)^d-FE_Q<d>(p)^d
  -FE_Nothing<d>()^d-FE_Nothing<d>()-FE_Nothing<d>()^d]
  Fluid FE Space: FESystem<d>[FE_Nothing<d>()^d-FE_Nothing<d>()^d
  -FE_Q<d>(p)^d-FE_Q<d>(p-1)-FE_Q<d>(p)^d]
Notes: Problem: 3 Finite element spaces of different sizes and potentially different orders, want to parameterize, current FESystems not implemented for larger than 5 objects
Step 46
Solution: Wrote an algorithm to combine FESystems, padding them with FE_Nothings of appropriate size into hp:Fecollections using the FETools::get_fe_from_name, which I had to modify to allow FESystems of arbitrary size (Note: Fluid and mesh are in the same System because they are on the same domain

## Slide 26: Partitioned coupling
Implementation
  Fluid: velocity continuity: constraints.set_inhomogeneity( … )
  Solid: traction continuity:
  Mesh: admissible displacements: constraints.set_inhomogeneity( … )
Convergence
  Aitken’s relaxation
Notes: Partitioned Implementation: treat as separate problems and solve normally with appropriate interface conditions Velocity continuity: add a constraint for each DOF on the interface of the fluid Traction continuity: add a term to the RHS of each DOF on the interface of the solid Mesh Displacements: add a constraint for each DOF on the interface of the fluid iterate to convergence Convergence: Aitkens relaxation of the solid promotes stability and convergence speed

## Slide 27: Monolithic coupling
Implementation:
  Fluid-Solid velocity continuity: constraints.add_line ( … ) constraints.add_entry ( … )
  Fluid-Solid: traction continuity: satisfied implicitly
  Mesh: admissible displacements
    Tried: same as velocity continuity (does not work)
    Tried: lagged displacement (works poorly)
    Tried: quasi-direct (works)
    Tried: Psuedo-strong coupling (works well!)
      weak coupling + constraints.set_inhomogeneity( … ) again
    Ideal: One-way constraint entry addition to the library
Convergence: Not Needed
Notes: For the Fluid-Solid velocity continuity in the monolithic case, we need to add lines to the constraint matrix and entries that tie the velocity dofs on the interface for the fluid and solid and set them equal We need to do this both when we build the original sparsity pattern and when actually performing the coupling
Problem with this: Requires 1 to 1 velocity dofs on the interface for the solid and fluid (same number, same order) constraints.add_line (solid_face_dof_indices[solid_vel_dof[i]]);
constraints.add_entry (solid_face_dof_indices[solid_vel_dof[i]], fl_msh_face_dof_indices[fluid_vel_dof[i]], 1.0);
Benefit of conforming velocity field. Automatically satisfies traction continuity
Second Issue: Mesh displacements We tried to do this the same way, only to realize that we did not in fact want two way coupling between the solid and mesh displacement Artificial stiffness
      Weakly enforce one-way coupling and then fix interface

## Slide 28: Future work
Parallelization!
Equal order elements for fluid
Adaptive meshes
Iterative algebraic solver
Various temporal discretizations
Different/Modern finite element techniques
Overset?

## Slide 29: Acknowledgements
deal.II workshop organizers
Naval Sea Systems Command, Advanced Submarine Systems Development Office (SEA 073R)
The Applied Research Laboratory at Pennsylvania State University

## Slide 30: Thank you
Questions?

## Slide 31: References
C. Michler, Computers & Fluids 33 , 839 (2004)
J. Degroote, K. Bathe, J. Vierendeels, Computers & Structures 87(11), 793 (2009)
M. Heil, Comput. Methods Appl. Mech. Engrg 193, 1 (2004)
S. Turek, J. Hron, Fluid-Structure Interaction pp. 371–385 (2006)

## Slide 32: Motivation Image Sources
Minehunter with composite prop image
  http://www.compositesworld.com/articles/composite-propeller-for-royal-navy-minehunter(2)
Lockheed Martin towed-array image
  http://www.lockheedmartin.com/data/assets/Towed_Array.pdf
Aortic valve model image
Arterial blood flow model image

## Slide 33: Bonus slides follow

## Slide 34: Spatial discretization

## Slide 35: Spatial discretization
Trial solution spaces
Weighting function spaces

## Slide 36: Residuals and Jacobians

## Slide 37: Convergence and relaxation
FSI iteration convergence
Newton-Raphson iteration convergence
Solid relaxation